I/O Ports

---
Keyboard & Mouse

---
AT-style keyboard

---
PC99 – Color Coding!
Mouse
(green)
Keyboard
(purple)

---
USB

---
USB Versions
- USB 1.0 / 1.1
  - “Low Speed” at
    1.5 Mbits/sec
  - “Full Speed” at
    12 Mbits/sec
  - Real-time (“isochronous”) is available when using “Full Speed”
- USB 2.0 / 2.1
  - Supports “Original USB” (aka 1.0/1.1) speeds
  - All devices must be backwards-compatible to 12Mbps
  - Adds “High Speed” at
    480 Mbits/sec

---
USB 1.1

---
Typical USB cables

---
USB Ports

---
Firewire

---
FireWire™ Versions
- IEEE 1394a
  - A.K.A. Sony i.Link
  - 400 Mbit/sec
  - “FireWire” is an Apple trademark equivalent to IEEE 1394a
- IEEE 1394b
  - 800 Mbit/sec
  - All 1394b devices (host and peripheral) are backwards compatible with 1394a

---
FireWire 400 / IEEE 1394a ports

---
FireWire 800 / IEEE 1394b port

---
Typical FireWire cables
FireWire 800

---
Video

---
13W3 Video
- Found in early workstations (Sun, Apollo, HP, etc.) until late 1990's
- Separate R, G, B coax lines ensured high signal quality

---
DB-15 / VGA
- Standard IBM PC VGA connector
- Requires heavy shielding for high resolutions
- Analog signals susceptible to interference

---
DVI (Digital Video Interface)
- Successor to VGA DB15 connector
- Can be analog or digital
- Approx 9 different types of DVI connector are NOT ALWAYS INTERCHANGEABLE!

---
HDMI
- Successor to DVI
- Can handle audio as well as video
- 100% digital interface

---
Audio

---
PC99 – color coding!
   Pink = microphone
Green = audio out (line-level)
   Blue = audio in (line-level)
Audio-out jack may also produce speaker-level voltage but if so, must be auto-detecting based on impedance.
Unfortunately, auto-detection doesn't always work!

---
http://support.creative.com/kb/ShowArticle.aspx?sid=3069

---
7.1 channel analog audio
1. Line Out 1 jack
2. Line Out 2 jack
3. Line Out 3 jack
4. Front Left
5. Front Right
6. Ground
7. Rear Left
8. Rear Right
9. Ground
10. Side Right
11. Center
12. Subwoofer
13. Ground
14. Side Left

---
Serial, Parallel, etc.
“DB”-style jacks

---
DB9
- Used for RS-232 (modems, mice)
- Monochrome video (IBM PC standard)
- Partial DB-9 (4 pins) sometimes used for FC-AL

---
DB25
- RS-232 Serial ports (modems, terminals)
- Centronics (printers)
- SCSI-1 (early Apple, Atari, Amiga, etc.)
  - Only usable at asynchronous speeds (5 MBytes/sec)

---
DB15
- Two-row type
  - AUI (ethernet)
- Three-row type
  - VGA (video)

---
DB50
Used for SCSI-1 applications, synchronous protocol up to 10 MBytes/sec

---
SCSI

---
SCSI-1
- Officially just “SCSI”
  - DB25
  - DB50
  - Centronics-50
- Up to 10MBytes/sec

---
SCSI-II
- Narrow (8-bit), up to 20 Mbytes/sec
- Wide (16-bit), up to 40 Mbytes/sec
- HD50 and HD68 connectors

---
SCSI-III
- Vast confusion of standards, ranging from 40 MBytes/sec to 640 Mbytes/sec
- Various high-density connectors, VHDCI is common for higher speeds

---
Other SCSI connectors...

---
Ethernet

---
AUI
Original 10Mbit/sec ethernet connection

---
AAUI (Apple AUI)
Remember the original embrace-and-extend people?

---
MII
- 100Mbit/sec version of AUI
- Found only on workstations from Sun, HP, etc. and certain routers (typically Cisco)
- Looks like SCSI-2 but isn't

---
GBIC
Successor to MII, for Gigabit networks

---
SFP
Small Form-factor Pluggable... for when GBICs are just too darn big.

---
XFP
or, 10-gigabit SFP

---
WTF?
- Yup, it's still ethernet.
- See the two SFP GBICs at the back of the card?
- Turns out PCI slots are almost wide enough to fit a SFP GBIC, but not quite.

---
Typical ethernet connectors