Title
Manitoba UNIX Users Group
Network Cabling for Dummies
Presented by Katherine Scrupa
September 11, 2012

---
Overview
Overview
- Why?
- Wired Options
- Cable Evolution
- Technical
- Troubleshooting

---
Why?
- Why bother when we have wireless?
- Why bother when we can buy a cable?
[Speaker Notes: Device doesn't have wireless (i.e. network printer) Reliability (conditions probably don't change much) Speed Collision domains (neighbours on same radio, other devices may use same wireless spectrum) Security (physical layer only) Wireless antenna throw / device antennati Distance Avoid interference RF/EMI Longer reach wireless susceptible to weather, moving leaves, rain Wiring at home with nice faceplates (impress your spouse and neighbours) Custom cables in a hurry Knowledge helps you troubleshoot problems]

---
Wired Options
Coaxial, BNC
UTP & STP / “RJ45”
(Copper, 8P8C)
Fiber
(lots... ST, SC, TOSLINK)
Power Lines!
[Speaker Notes: 8p8c = "eight positions, eight conductors"]

---
Cable Evolution
[Speaker Notes: Unshielded twisted pair Shielded twisted pair To avoid Electomagnetic Interference Causes of EMI Devices Machinery, factory environments Some lights!]

---
Cable Evolution
Copper vs Fiber
[Speaker Notes: Fiber is light, not electrical; not susceptible to EMI Length is a plus 550m or 5km instead of 100m Not as bendy]

---
Cable Evolution
- Environmental Ratings
- CMP	Communications Plenum
- CMR	Communications Riser
- CMG	Communications General purpose
- CM	Communications
- CMX	Communications Residential
- CMH	CSA FT1
[Speaker Notes: Describe plenum CMR (Communications Riser), insulated with high-density polyolefin and jacketed with low-smoke polyvinyl chloride (PVC) can be replaced by a CMP (Communications Plenum), insulated with fluorinated ethylene propylene (FEP) and polyethylene (PE) and jacketed with low-smoke polyvinyl chloride (PVC), due to better flame test ratings. CM (Communications) is insulated with high-density polyolefin, but not jacketed with PVC and therefore is the lowest of the three in flame resistance "UV-rated" or "UV-stable usually made with pvc Gel filled or sealed cables suitable for direct burial (keep out moisture) Plenum-rated cables are slower to burn and produce less smoke than pvc (may affect sprinkler system requirements in an area]

---
Cable Evolution
- Cat5 (100 MHz)
- Cat5e (100 MHz)
  - stricter testing than Cat 5
Cat6 (250 MHz)
  - even more resilient to crosstalk and noise
Cat6a (500 MHz)
  - maximum 100m for up to Gigabit Ethernet, 55m for 10Gigabit.
  - More resilient to alien crosstalk
[Speaker Notes: Alien crosstalk = EMI originating from outside the calbe]

---
Cable Evolution
Speeds
Common Name	Speed	Technical Name	Medium	Max Length
Ethernet	10Mbps	10Base-T	Copper	100m
Fast Ethernet	100Mbps	100Base-TX	Copper	100m
Gigabit Ethernet	1000Mbps	1000Base-SX / 1000Base-LX	Fiber	550m (SX) / 5km (LX)
Gigabit Ethernet	1000Mbps	1000Base-T	Copper	100m
[Speaker Notes: Max length suggested... YOU'VE BEEN WARNED 100m may not be as long as you think when you're running it up and down walls, to wiring closets etc.]

---
RJ45 Technical (“Fluffy”)
- Boots
- Faceplates and keystones
- Patch cables, keystone & patch panels
- Minimum bend 1 inch	(Demo - What NOT to do with your cable)
- Colours
- 8 wires
- Twists per inch
[Speaker Notes: Boots (cover tab to prevent snapping) Keystone snap in faceplate Crimp for patch cable, punch down for keystone and patch panel, router NIC throughput (megabit switch with 24 ports = 100Mbps x 24 = 24Mbps or 2.4 Gbps potential throughput) Gbic hwic card slot to update an old router Demo (wrap, corners & yanking, making magnets, untwist and damages wires) Colours and vlans, creating “virtual multiple switches” per switch (encapsulation and traffic boundary), picking one colour for crossovers 8 wire colours Twists in each set cancels directional emi (opposing) Twists per set vary Don't untwist more than necessary NEXT, cable stats]

---
RJ45 Technical (“Hard”)
  EIA/TIA specifications
  T568A	T568B
[Speaker Notes: electrical/telecommunications industry Canmake a “straight through cable” with either, as long as both ends the same type (A+A or B+B) A is common/standard Crossover made from one of each EIA/TIA standard (A and B) Read as greenwhite, green, orangewhite, blue, bluewhite, orange, brownwhite, brown For Ethernet (10Mbps) and FastEthernet (100Mbps), only four wires/pins are used (1, 2, 3, 6) Yup, everything else doing nothing]

---
RJ45 Technical (“Hard”)
Gigabit copper – two crossovers!

---
Straight Through vs Crossover Usage
Send on 1,2 receive on 3,6		Send on 3,6 receive on 1,2
PC NICs		Hubs
Routers		Switches
Wireless Access Point
Networked Printers
[Speaker Notes: Just remember “hubs and switches” If you're connecting devices in the same column, you need crossover. Otherwise, send and receive needs straight through because something sent from those pins ends up getting received on the right pins on the other end. What do you use to connect to your “router” at home. BTW, is a bastardization of a router. Auto-MDIX, just to mess withyou (it auto fixes your mistakes, need for crossover cables) Good to know what SHOULD be used, regardless.]

---
Troubleshooting
“Layer 1”
  - Plugged in / good connection?
  - Right cable for right device?
  - Keystone pin connectors, punchdown check
- Cable testers
- Swap cable or device (jitter/jabber)
- Site Survey
[Speaker Notes: Check keystone contacts aren't bent Jitter or jabber will either be caused by the cable or device Site survey – any EMI interference around? Lights, metal, other cables or electrical. A/C turning on on roof. Abuses to cable (vaccuum cleaners, carts, etc)]

---
Thanks / Image Sources
- user Meggar (Wikipedia), GPL 1.2
- David Monniaux, GPL 1.2
- Adam Antios, GPL 1.2
- Uwe Schwöbel, GPL 1.2
- Hustvedt, GPL 1.2
- public domain